## Slide 1: Internet Architecture & Performance
Cs 4850

## Slide 2: Recap of Previous Lecture - Strategies
Addressing
Routing
Multiplexing

## Slide 3: Machinery (cont)
Multiplexing and Demultiplexing (demux key)
Encapsulation (header/body)
Host
Host
Application
program
Application
program
RRP
Data
Data
HHP
RRP
HHP
Application
program
Application
program
RRP Data
RRP Data
HHP RRP Data

## Slide 4: Internet Protocol Stack
application: supporting network applications
  ftp, smtp, http
transport: host-host data transfer
  tcp, udp
network: routing of datagrams from source to destination
  ip, routing protocols
link: data transfer between neighboring network elements
  ppp, ethernet
physical: bits “on the wire”
application
transport
network
link
physical

## Slide 5: Layering: Logical Communication
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
data
data
E.g.: transport
take data from app
add addressing, reliability check info to form “datagram”
send datagram to peer
wait for peer to ack receipt
analogy: post office
data
transport
transport
ack

## Slide 6: Layering: Physical Communication
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
data
data

## Slide 7: ISO Architecture
The ISO was one of the first organizations to formally define a common way to connect computers
Open Systems Interconnection (OSI)
Defines a partitioning of network functionality into seven layers
One or more protocols implement the functionality assigned to a given
Notes: The ISO was one of the first organizations to formally define a common way to connect computers. Their architecture, called the Open Systems Interconnection (OSI) architecture and illustrated in Figure 1.13, defines a partitioning of network functionality into seven layers, where one or more protocols implement the functionality assigned to a given layer. In this sense, the schematic given in Figure 1.13 is not a protocol graph, per se, but rather a reference model for a protocol graph. It is often referred to as the 7-layer model.

## Slide 8: ISO Architecture
The physical layer handles the transmission of raw bits over a communications link.

## Slide 9: ISO Architecture
Data link layer collects a stream of bits into a larger aggregate called a frame. Network adaptors, along with device drivers running in the node’s operating system, typically implement the data link level

## Slide 10: ISO Architecture
Network layer handles routing among nodes within a packet-switched network. At this layer, the unit of data exchanged among nodes is typically called a packet rather than a frame, although they are fundamentally the same thing.

## Slide 11: ISO Architecture
Transport layer then implements what a process-to-process channel. The unit of data exchanged is commonly called a message rather than a packet or a frame. The transport layer and higher layers typically run only on the end hosts and not on the intermediate switches or routers.

## Slide 12: ISO Architecture
Session layer provides a name space that is used to tie together the potentially different transport streams that are part of a single application. For example, it might manage an audio stream and a video stream that are being combined in a teleconferencing application

## Slide 13: ISO Architecture
Presentation layer is concerned with the format of data exchanged between peers—for example, whether an integer is 16, 32, or 64 bits long, whether the most significant byte is transmitted first or last, or how a video stream is formatted.

## Slide 14: ISO Architecture
Application layer protocols include things like the Hypertext Transfer Protocol (HTTP), which is the basis of the World Wide Web and is what enables web browsers to request pages from web servers

## Slide 15: Internet Architecture
Defined by Internet Engineering Task Force (IETF)
Hourglass Design
Application vs Application Protocol (FTP, HTTP)
Also called TCP/IP
Evolved out of experiences with an earlier packet-switched network called the ARPANET.
Internet and the ARPANET were funded by the Advanced Research Projects Agency (ARPA),
■ ■ ■
FTP
TCP
UDP
IP
NET
1
NET
2
NET
n
HTTP
NV
TFTP
Notes: NV, TFTP? Trivial FTP.
X.25 is a packet switched data network protocol which defines an international recommendation for the exchange of data as well as control information between a user device (host), called Data Terminal Equipment (DTE) and a network node, called Data Circuit Terminating Equipment (DCE).
X.500 is a distributed directory protocol which allows hierarchies of countries, regions, organizations, and individuals to be catalogued.

## Slide 16: Internet Architecture
Defined by Internet Engineering Task Force (IETF)
Hourglass Design
Application vs Application Protocol (FTP, HTTP)
■ ■ ■
FTP
TCP
UDP
IP
NET
1
NET
2
NET
n
HTTP
NV
TFTP
Notes: NV, TFTP? Trivial FTP.
X.25 is a packet switched data network protocol which defines an international recommendation for the exchange of data as well as control information between a user device (host), called Data Terminal Equipment (DTE) and a network node, called Data Circuit Terminating Equipment (DCE).
X.500 is a distributed directory protocol which allows hierarchies of countries, regions, organizations, and individuals to be catalogued.

## Slide 17: Internet Architecture Alt
The Internet architecture does not imply strict layering. The application is free to bypass the defined transport layers and to directly use IP or one of the underlying networks. In fact, programmers are free to define new channel abstractions or applications that run on top of any of the existing protocols.

## Slide 18: Implications of Hourglass
A single Internet layer module:
Allows all networks to interoperate
  all networks technologies that support IP can exchange packets
Allows all applications to function on all networks
  all applications that can run on IP can use any network
Simultaneous developments above and below IP
■ ■ ■
FTP
TCP
UDP
IP
NET
1
NET
2
NET
n
HTTP
NV
TFTP
This shape actually reflects the central philosophy of the architecture. That is, IP serves as the focal point for the architecture— it defines a common method for exchanging packets among a wide collection of networks. Above IP there can be arbitrarily many transport protocols, each offering a different channel abstraction to application programs. Thus, the issue of delivering messages from host to host is completely separated from the issue of providing a useful process-to-process communication service.

## Slide 19: Principle of Internet Architecture
A final attribute of the Internet architecture (or more accurately, of the IETF culture) is that in order for a new protocol to be officially included in the architecture, there must be both a protocol specification and at least one (and preferably two) representative implementations of the specification. The existence of working implementations is required for standards to be adopted by the IETF
“We reject Kings, Presidents and voting. We believe in rough consensus and running code”

## Slide 20: Performance Metrics
Bandwidth (throughput)
  data transmitted per time unit
  link (e.g, 10Mbps) versus end-to-end (effective bandwidth, or throughput) (e.g., 2.2Mbps)
  notation
    KB = 210 bytes
    Mbps = 106 bits per second
Latency (delay)
  time to send message from point A to point B
  one-way versus round-trip time (RTT)
  components
    Latency = Transmit + Propagation + Queue
    Propagation = Distance / c
    Transmit = Size / Bandwidth (time to put the data on link)

## Slide 21: Bandwidth versus Latency
Relative importance
  1-byte: 1ms vs 100ms dominates 1Mbps vs 100Mbps
  25MB: 1Mbps vs 100Mbps dominates 1ms vs 100ms
Infinite bandwidth
  RTT (measured using a small size packet) dominates
    Throughput = TransferSize / TransferTime
      Also called effective bandwidth
    TransferTime = RTT + TransferSize/Bandwidth
  1-MB file to 1-Gbps link as 1-KB packet to 1-Mbps link

## Slide 22: Delay x Bandwidth Product
Amount of data “in flight” or “in the pipe”
Usually relative to RTT
Example: 100ms x 45Mbps = 560KB

## Slide 23: Exercise
Calculate the total time required to transfer a 1.5 MB file, assuming an RTT of 80 ms, a packet size of 1 KB, and an initial 2xRTT of “hand-shaking” before data is sent. The bandwidth is 10 Mbps, but after finishing sending each data packet, must wait one RTT before sending the next. Assume transfer is completed when last packet arrives.
Sol:
  # of packets=1.5MB/1KB=1536
  # of RTTs between when packet 1 arrives and packet 1536 arrives=1535
  Total time= 2RTT (handshake) +1.5x2^20x8 /10,000,000+1535 RTT (waiting)+RTT/2 (propagation)=124.258 second
What is the effective bandwidth (or throughput)?

## Slide 24: Exercise
The bandwidth is 10 Mbps, and data packets can be sent continuously.
The link allows infinitely fast transmit, but limits bandwidth such that only 20 packets can be sent per RTT.
Zero transmit time as in (c), but during the first RTT we can send one packet, during the second RTT we can send two packets, during the third we can send four (2^(3−1)), etc

## Slide 25: Exercise
Consider a point-to-point link 50 km in length. At what bandwidth would propagation delay (at a speed of 2×10^8m/s) equal transmit delay for 100-byte packets? What about 512-byte packets?