## Slide 1: Reliable Transmission
Sliding Window

## Slide 2
Outline
  Encoding
  Framing
  Error Detection
  Sliding Window Algorithm
Point-to-Point Links Slides adapted from Larry Peterson

## Slide 3: Reliable Transmission
Some error codes are strong enough also to correct errors, in practice the overhead is typically too large to handle the range of bit and burst errors
Even when error-correcting codes are used (e.g., on wireless links) some errors will be too severe to be corrected.
Some corrupt frames must be discarded
A link level protocol that wants to deliver frames reliably must somehow recover from these discarded (lost) frames.

## Slide 4: Reliable Transmission
Reliability is handled at varying layers but the principles are consistent
  Handles by acknowledgements and timeouts
  An ACK is a control frame…header only
  Using ACK’s and timeouts is often called Automatic Repeat Requests

## Slide 5: Acknowledgements & Timeouts
Duplicated frame
Duplicated frame

## Slide 6: Acknowledgements & Timeouts
include 1-bit sequence number
Duplicated frame
Duplicated frame

## Slide 7: Stop and Wait Algorithm
Simplest ARQ scheme
After transmitting one frame, the sender waits for an acknowledgment before transmitting the next frame
If the acknowledgment does not arrive after a certain period of time
  sender times out and retransmits the original frame
Potential to cause duplicate copies of a frame to be delivered
header for a stop-and-wait protocol usually includes a 1-bit sequence number
Sequence numbers alternate

## Slide 8: Stop-and-Wait
Problem: keeping the pipe full
Example
  1.5Mbps link x 45ms RTT = 67.5Kb (8KB)
  1KB frames implies 1/8th link utilization
Sender
Receiver

## Slide 9: How can we improve Stop and Wait

## Slide 10: Sliding Window
Allow multiple outstanding (un-ACKed) frames
Upper bound on un-ACKed frames, called window
How to determine the value of “window”?
  Filling the pipe
Notes: Needs to keep track of # of outstanding packets.

## Slide 11: SW: Sender
Assign sequence number to each frame (SeqNum)
Maintain three state variables:
  send window size (SWS): bound on # of outstanding/unAcked frames
  last acknowledgment received (LAR)
  last frame sent (LFS)
Maintain invariant: LFS - LAR <= SWS
Advance LAR when ACK arrives
Buffer up to SWS frames (for retransmission if necessary)
<
SWS
LAR
LFS
■ ■ ■
■ ■ ■
─

## Slide 12: SW: Receiver
Maintain three state variables
  receive window size (RWS<=SWS): bound on # of out-of-order frames
  largest acceptable frame (LAF)
  last frame received & Acked (LFR)
Maintain invariant: LAF - LFR <= RWS
Frame SeqNum arrives:
  if LFR < SeqNum < = LAF accept
  if SeqNum < = LFR or SeqNum > LAF discarded
Send cumulative ACKs
  Ack only the last received frame whose previous frames have all been received.
RWS
LFR
LAF
■ ■ ■
■ ■ ■
<
─

## Slide 13: Timeline Diagram for Sliding Window
SWS=RWS=3 frames
Timeout= 2 RTT
2 RTT
1 RTT
3 RTT
Frame[1]
Frame[2]
Frame[3]
ACK[1]
ACK[2]
ACK[3]
Frame[4]
Frame[5]
Frame[6]
X
Frame[4]
Frame[5]
Frame[6]
ACK[6]
Frame[7]
Could resend ACK 3 here
Cumulative ACK

## Slide 14: Example
Draw a timeline diagram for the sliding window algorithm with SWS = RWS = 4 frames in the following two situations. Assume the receiver sends a duplicate acknowledgment if it does not receive the expected frame. For example, it sends DUPACK[2] when it expects to see Frame[2] but receives Frame[3] instead. Also, the receiver sends a cumulative acknowledgment after it receives all the outstanding frames. For example, it sends ACK[5] when it receives the lost frame Frame[2] after it already received Frame[3], Frame[4], and Frame[5]. Use a timeout interval of about 2×RTT
Frame 2 is lost. Retransmission takes place upon timeout (as usual).
Frame 2 is lost. Retransmission takes place either upon receipt of the first DUPACK or upon timeout. Does this scheme reduce the transaction time?

## Slide 15: Timeline Diagram for Sliding Window
SWS=RWS=4 frames
Timeout= 2 RTT
2 RTT
1 RTT
3 RTT
Frame[1]
Frame[2]
Frame[3]
ACK[1]
Frame[5]
X
Frame[2]
Frame[3]
Frame[4]
ACK[5]
Frame[6]
Cumulative ACK
Frame[4]
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Frame[5]
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Frame[7]
Frame[8]
Frame[9]
4 RTT

## Slide 16: Timeline Diagram for Sliding Window
SWS=RWS=4 frames
Timeout= 2 RTT
2 RTT
1 RTT
3 RTT
Frame[1]
Frame[2]
Frame[3]
ACK[1]
Frame[5]
X
Frame[6]
Cumulative ACK
Frame[4]
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Frame[7]
Frame[8]
Frame[9]
4 RTT
DUPACK[2]
Frame[2]
ACK[5]

## Slide 17: Sequence Number Space
SeqNum field is finite; sequence numbers wrap around
Sequence number space must be larger than number of outstanding frames
SWS <= MaxSeqNum-1 is not sufficient
  suppose 3-bit SeqNum field (0..7)
  SWS=RWS=7
  sender transmit frames 0..6
  arrive successfully, but ACKs lost
  sender retransmits 0..6
  receiver expecting 7, 0..5, but receives first incarnation of 0..5
SWS <(MaxSeqNum+1)/2 is correct rule (if SWS=RWS)
  What if RWS!=SWS? Your exercise !
Intuitively, SeqNum “slides” between two halves of sequence number space

## Slide 18: Concurrent Logical Channels
Multiplex 8 logical channels over a single link
Run stop-and-wait on each logical channel
Maintain three state bits per channel (in implementation)
  channel busy
  current sequence number out
  next sequence number in
Header: 3-bit channel num, 1-bit sequence num
  4-bits total
  same as sliding window protocol (for sequence #)
Separates reliability from order
Notes:   Used in ARPANET, frames sent over a given link not kept in any particular order.
  next sequence number in: expected on a frame that arrives on this channel

## Slide 19
Summary of supported functions:
  Encoding
  Framing
  Error Detection
  Sliding Window Algorithm
Point-to-Point Links

## Slide 20: Reading
Chapter 2: 2.2, 2.3, 2.4(2.4.2, 2.4.3), 2.5

## Slide 21: Timeline Diagram for Sliding Window
SWS=RWS=3 frames
Timeout= 2 RTT