## Slide 1
  Point-to-Point Links
  Shared Access Networks
Direct Link Networks
■ ■ ■
FTP
TCP
UDP
IP
NET
1
NET
2
NET
n
HTTP
NV
TFTP
Our goals:
understand principles behind data link layer services:

## Slide 2
Outline
  Encoding
  Framing
  Error Detection
  Sliding Window Algorithm
Point-to-Point Links Slides adapted from Larry Peterson

## Slide 3: Signalling

## Slide 4: Encoding
Signals propagate over a physical medium
  modulate electromagnetic waves
  e.g., vary voltage
Encode binary data onto signals
  e.g., 0 as low signal and 1 as high signal
  known as Non-Return to zero (NRZ)

## Slide 5: Problem: Consecutive 1s or 0s
Low signal (0) may be interpreted as no signal
High signal (1) leads to baseline wander
Unable to recover clock
Notes: Baseline wander: average signal biased to low or high.
Frequent transition is necessary for clock recovery/synchronization, to avoid clock drift.

## Slide 6: Problem: Consecutive 1s or 0s
Low signal (0) may be interpreted as no signal
High signal (1) leads to baseline wander
  the receiver keeps an average of the signal it has seen so far and then uses this average to distinguish between low and high signals.
  signal is significantly lower than this average = 0
  Higher than average signal = 1
The problem, of course, is that too many consecutive 1s or 0s cause this average to change, making it more difficult to detect a significant change in the signal
Notes: Baseline wander: average signal biased to low or high.
Frequent transition is necessary for clock recovery/synchronization, to avoid clock drift.

## Slide 7: Problem: Consecutive 1s or 0s
Unable to recover clock
  frequent transitions from high to low and vice versa are necessary to enable clock recovery
  both the encoding and the decoding processes are driven by a clock
  every clock cycle the sender transmits a bit and the receiver recovers a bit
  sender and the receiver clocks have to be precisely synchronized in order for the receiver to recover the same bits the sender transmits
  If the receiver’s clock is even slightly faster or slower than the sender’s clock, then it does not correctly decode the signal
How to fix the clock problem?
Notes: Baseline wander: average signal biased to low or high.
Frequent transition is necessary for clock recovery/synchronization, to avoid clock drift.

## Slide 8: Alternative Encodings
Non-return to Zero Inverted (NRZI)
  make a transition from current signal to encode a one; stay at current signal to encode a zero
  solves the problem of consecutive ones
Manchester
  transmit XOR of the NRZ encoded data and the clock
  only 50% efficient (bit rate = 1/2 baud rate)
Notes: Baud rate: the rate at which signal changes.

## Slide 9: Encodings (cont)

## Slide 10: Alternative Encodings
Non-return to Zero Inverted (NRZI)
  make a transition from current signal to encode a one; stay at current signal to encode a zero
  solves the problem of consecutive ones
Manchester
  transmit XOR of the NRZ encoded data and the clock
  only 50% efficient (bit rate = 1/2 baud rate)
Notes: Baud rate: the rate at which signal changes.

## Slide 11: Encodings (cont)

## Slide 12: Encodings (cont)
4B/5B
  every 4 bits of data encoded in a 5-bit code
  5-bit codes selected to have no more than one leading 0 and no more than two trailing 0s
  thus, never get more than three consecutive 0s
  resulting 5-bit codes are transmitted using NRZI
  achieves 80% efficiency

## Slide 13: 4B/5B

## Slide 14: Framing
Break sequence of bits into a frame
Typically implemented by network adaptor