## Slide 1: Framing & Error Checking
Recap of Encoding
Framing Methods
Parity
Checksum
CRC

## Slide 2: Recap****
Encoding
  NRZ: 1’s and zeros. Consecutive zeros wouldn’t keep clock in sync
  NRZI: non-return to zero inverted. make a transition from current signal to encode a one; stay at current signal to encode a zero. Solves the problem of consecutive ones
  Manchester Encoding: solved issues of transitioning. 1’s are low to high 0’s are high to low. Inefficient because transition of signal doesn’t necessarily mean a change in information. Solves consecutive 1’s and 0’s
  4B/5B: 4 bit/ 5bit: NRZI but can only have one zero in 4 bit and transfers it to 5 bit codes
Notes: Encoding: how to get information
NRZ: 1’s and zeros

## Slide 3: Framing
Break sequence of bits into a frame
Typically implemented by network adaptor

## Slide 4: Approaches
Sentinel-based
  Place special characters to indicate where characters begin and end
  SYN – beginning of frame
  STX - Start of Text
  ETX – End of Text
  SOH – Start of Header
Notes: HDLC, SDLC? High-level data link control, synchronous data link control
Sentinel: guard, watch

## Slide 5: Approaches
Sentinel-based
  delineate frame with special pattern: 01111110
    Also sent during idle link time
  e.g., HDLC (high level), SDLC (synchronous), PPP
  Problem?
  special pattern appears in the payload
  solution: bit stuffing
    sender: (always) insert 0 after five consecutive 1s
    receiver: delete 0 that follows five consecutive 1s
Notes: HDLC, SDLC? High-level data link control, synchronous data link control
Sentinel: guard, watch

## Slide 6: Approaches (cont)
Counter-based
  include payload length in header
  e.g., DDCMP
  problem: count field corrupted
  solution: catch when CRC fails
Notes: DDCMP:digital data communication message protocol

## Slide 7: Approaches (cont)
Clock-based
  each frame is 125us long
  e.g., SONET: Synchronous Optical Network
  STS-n (STS-1 = 51.84 Mbps)
Notes: STS: synchronous transport signal
810 bytes

## Slide 8
Outline
  Encoding
  Framing
  Error Detection
  Sliding Window Algorithm
Point-to-Point Links
■ ■ ■
FTP
TCP
UDP
IP
NET
1
NET
2
NET
n
HTTP
NV
TFTP

## Slide 9: Error Detection
Add redundant information to a frame that can be used to determine if errors have been introduced.
The goal of error detecting codes is to provide a high probability of detecting errors combined with a relatively low number of redundant bits.
Redundant bits derived from the original message using a well defined algorithm
Sender and receiver agree on the algorithm

## Slide 10: Parity
Even or odd parity

## Slide 11: Internet Checksum Algorithm
View message as a sequence of 16-bit integers; sum using 16-bit ones-complement arithmetic; take ones-complement of the result.
Attach the checksum with the original message
u_short
cksum(u_short *buf, int count)
{
register u_long sum = 0;
while (count--)
{
sum += *buf++;
if (sum & 0xFFFF0000)
{
/* carry occurred, so wrap around */
sum &= 0xFFFF;
sum++;
}
}
return ~(sum & 0xFFFF);
}
Notes: 25 11 12 7 13 4
=72
Chksum = 16
72/16 = (only concerned w/ the remainder)= Remainder = 8
The receiver sends 25 11 12 7 13 4 +(R8)
If the receiver gets an 8 at the end, then everything is good. Else message gets corrupted

## Slide 12: Cyclic Redundancy Check (Error Detection)
Add k bits of redundant data to an n-bit message
  want k << n
  e.g., k = 32 and n = 12,000 (1500 bytes)
Represent n-bit message as n-1 degree polynomial
  e.g., MSG=10011010 as M(x) = x7 + x4 + x3 + x1
Let k be the degree of some divisor polynomial
  e.g., C(x) = x3 + x2 + 1

## Slide 13: CRC (cont)
Transmit polynomial P(x) that is evenly divisible by C(x)
  shift left k bits, i.e., M(x)xk
  subtract remainder of M(x)xk / C(x) from M(x)xk
  i.e., P(x)= M(x)xk – (remainder of M(x)xk / C(x))
Receiver polynomial P(x) + E(x)
  E(x) = 0 implies no errors
Divide (P(x) + E(x)) by C(x); remainder zero if:
  E(x) was zero (no error), or
  E(x) is exactly divisible by C(x)

## Slide 14: CRC Example
Message M(x): x7+x4+x3+x1 10011010
C(x)=1101
Multiply by X3 10011010000
      11111001
  1101 10011010000
      1101
      1001
      …
      101 remainder
Send 10011010101
Binary division
Notes: M(x) = 10011010
C(x) = 1101

## Slide 15: Selecting C(x) (with degree of k)
Can detect all single-bit errors, as long as the xk and x0 terms have non-zero coefficients.
Can detect all double-bit errors, as long as C(x) contains a factor with at least three terms
Can detect any odd number of errors, as long as C(x) contains the factor (x + 1)
Can detect any ‘burst’ error (i.e., sequence of consecutive error bits) for which the length of the burst is less than k bits.
Most burst errors of larger than k bits can also be detected
See Table 2.5 on page 96 for common C(x)